## Slide 1
solcomplex2realDefinite.tex
MIMO Robust Stability
Introduction
ESA, February 2014
Copyright 2007-14, MUSYN. This work is licensed under the Creative Commons Attribution- NonCommercial-ShareAlike 3.0 Unported License. To view a copy of this license, visit http://creativecommons.org/licenses/by-nc-sa/3.0/ or send a letter to Creative Commons, 444 Castro Street, Suite 900, Mountain View, California, 94041, USA.

## Slide 2: Multivariable Nyquist
Simplest approach starts with underlying state-space model, and relates internal stability of closed-loop system to graphical frequency-domain condition.
MVNyquist: Assume A has no imaginary-axis eigenvalues. The closed-loop system is internally stable if-and-only-if the Nyquist plot of
does not pass through the origin, and encircles the origin nu times counterclockwise, where nu is the number (counting multiplicity) of unstable eigenvalues of A.
Proof: Closed-loop dynamics are . Determinant identity (over the field of rationals) gives
Standard “Principal of the argument” finishes the proof.

## Slide 3: Multivariable Nyquist, 2 systems
Two-block interconnection
can be viewed as unity-feedback around concatenated system
Note:

## Slide 4: Multivariable Nyquist, usual plant/controller interpretation
MIMO Plant/Controller
can be viewed as unity-feedback around concatenated system
Note:
P
C

## Slide 5: Effect of uncertainty at plant input
Plant, P
  Linear, time invariant
Controller, C
  Linear, time-invariant
  Stabilizes P
Uncertainty in P
  Uncertain gain (complex matrix) at input
Question: What is the smallest such that feedback interconnection of and is unstable?
Nyquist plot of det(I+PC)
  does not pass through 0
  encircles 0 the correct number of times, CCW
P
C
P
Δ
More realistic uncertainty models later

## Slide 6: Effect of uncertainty at plant input
Perturbed closed-loop system
Perturbed plant, P(I+Δ)
  unstable poles: same as unstable poles of P
  hence, same number of unstable poles
Controller, C
  Linear, time-invariant
  Stabilizes P
  Stabilizes P(I+Δ)
P
C
Δ
Nyquist plot of det(I+P(I+Δ)C)
  does not pass through 0
  encircles 0 the correct number of times, CCW

## Slide 7: Effect of uncertainty at plant input
Plant, P(I+Δ)
  Linear, time invariant
Controller, C
  Linear, time-invariant
  Stabilizes P
Question: What is the smallest such that feedback interconnection of and is unstable?
Equivalently (since Δ is constant): What is smallest Δ such that Nyquist plot of det(I+P(I+Δ)C)
  passes through the origin, 0, or
  encircles 0 the incorrect number of times?
    incorrect ↔ different than the #encirclements by det(I+PC)
det(I+P(I+Δ)C)) is continuous in Δ
  This warps the Nyquist plot continuously
  Encirclements transition from correct→incorrect by passing through 0
Nyquist plot of det(I+PC)
  does not pass through 0, and
  encircles 0 the correct number of times, CCW
-3
-2
-1
0
1
2
3
0
1
2
3
4

## Slide 8: Effect of uncertainty at plant input
Plant, P(I+Δ)
  Linear, time invariant
Controller, C
  Linear, time-invariant
  Stabilizes P
What is smallest Δ such that
  Nyquist plot of det(I+P(I+Δ)C) passes through 0?
  Approach: Solve independently at each frequency
  Find “worst” frequency
Nyquist plot of det(I+PC)
  does not pass through 0, and
  encircles 0 the correct number of times, CCW

## Slide 9
[U,S,V] = svd(M);
Delta = (-1/S(1,1))*V(:,1)*U(:,1)’;

## Slide 10: Effect of uncertainty at plant input
What is smallest Δ such that
  Nyquist plot of det(I+P(I+Δ)C) passes through 0?
  Solve independently at each frequency
  Find “worst” frequency (with smallest such Δ)
“Easiest” location for pole to migrate from stable to unstable is at this frequency

## Slide 11: Interpretation of Robustness Margin
Plant, Controller, P, C
  Linear, time invariant
  C Stabilizes P
Robustness of Stability
  What is the smallest (complex matrix) Δ such that feedback of P(I+Δ) and C is unstable?
Code: Given P and C
P
C
Δ
P
C
H = loopsens(P,C)
[TiNorm,freq] = norm(H.Ti,inf,0.001);
M = freqresp(H.Ti,freq);
[U,S,V] = svd(M); Delta = -1/S(1,1)*V(:,1)*U(:,1)’;
pole(feedback(P*(eye(size(P,2))+Delta),C))
freq
[norm(Delta) 1/TiNorm]
See exercise: DestabilizingUncertainty

## Slide 12: Interpretation of Robustness Margin
Plant, Controller, P, C
  Linear, time invariant
  C Stabilizes P
Robustness of Stability
  What is the smallest (complex matrix) Δ such that feedback of P(I+Δ) and C is unstable?
P
C
Δ
P
C
P
C
Δ
P
C
What does Δ interact with?

## Slide 13: Δ is in feedback with
Plant, Controller, P, C
  Linear, time invariant
  C Stabilizes P
Robustness of Stability
  What is the smallest (complex matrix) Δ such that feedback of P(I+Δ) and C is unstable?
P
C
Δ
P
C
P
C
Δ
P
C
Δ
Uncertain closed-loop system represented as feedback between known and unknown part
Remember this picture

## Slide 14: Relation to distance of det(I+PC) to 0
Are these the same idea?
There exists small Δ to make det(I+P(I+Δ)C) = 0
det(I+PC) ≈ 0
?
-2
0
2
4
6
-4
-3
-2
-1
0
1
2
3
4
Real
Imag
Nyquist plot of L
L
-2
0
2
4
6
-4
-3
-2
-1
0
1
2
3
4
Real
Imag
Nyquist plot of 1+L
1+L
-2
0
2
4
6
-4
-3
-2
-1
0
1
2
3
4
Real
Imag
Nyquist plot of det(I+Lk), k=1, 2, ...
No!
Multivariable Nyquist plot passes close to 0

## Slide 15: Richer, more expressive uncertainty models
Constant weighting matrices WL and WR as part of model
  Uncertainty is not uniform across all input channels
  Smallest Δ such that feedback of P(I+WLΔWR) and C is unstable?
What is smallest Δ such that
  Nyquist plot of det(I+ P(I+WLΔWR) C) passes through 0?
  Solve independently at each frequency
Can also make the WL and WR as frequency-dependent…

## Slide 16: Richer, more expressive uncertainty models
Stable weighting systems WL(s) and WR(s) as part of model
  Uncertainty has limited dependence on frequency
  Smallest Δ such that feedback of P(I+WLΔWR) and C is unstable?
What is smallest Δ such that
  Nyquist plot of det(I+ P(I+WLΔWR) C) passes through 0?
  Solve independently at each frequency

## Slide 17: Transition from constant→dynamic uncertainty
Nominal Plant, P
  Linear, time invariant
Controller, C
  Linear, time-invariant
  Stabilizes P
Uncertainty in P
  Uncertain gain at input (constant, complex matrix Δ)
  Uncertain dynamics at input (stable, real, linear system, )
P
C
WL
Δ
P
WR
Nyquist argument still applies, construction of smallest destabilizing Δ is more involved.
Notation

## Slide 18: Real Dynamic models mimicking Complex numbers
deltaNum = complex(randn,randn)
deltaNum =
-9.8847e-001 +1.3156e+000i
w = exp(3*randn)
w =
1.2535e+000
deltaSys = cnum2sys(deltaNum,w);
zpk(deltaSys)
Zero/pole/gain:
1.6455 (s-2.51)
---------------
(s+2.51)
[norm(deltaSys,inf) abs(deltaNum)]
ans =
1.6455e+000 1.6455e+000
freqresp(deltaSys,w)
ans =
-9.8847e-001 +1.3156e+000i
cnum2sys

## Slide 19: Relation between complex and real-rational uncertainty
For linear, uncertain systems, the “equivalence” between
  Constant, complex, uncertainty, and
  Linear, dynamic (with real coefficients)
can be established. For a SISO system…
Given stable, SISO G(s) and constants
  there exists a complex scalar Δ with such that feedback connection of (G,Δ) has a pole at
if and only if
  there exists a stable linear system (with real coefficients) satisfying
  and the feedback connection of has a pole at

## Slide 20: Relation between complex and real-rational uncertainty
For linear, uncertain systems, the “equivalence” between
  Constant, complex, uncertainty, and
  Linear, dynamic (with real coefficients)
can be established.
Given stable, MIMO G(s) and constants
  there exists a complex matrix Δ with such that feedback connection of (G,Δ) has a pole at
if and only if
  there exists a linear system (with real coefficients) satisfying
  and the feedback connection of has a pole at
Proof is more complicated than SISO case, but involves a similar “interpolation approach. It is outlined in the next three slides.

## Slide 21: Stability of Feedback Interconnection

## Slide 22: Real Dynamic models mimicking Complex matrices
Given complex vectors u, v and a real scalar .
The statements below are equivalent:
  There exists a complex matrix Δ, with
  The euclidean norms satisfy
  For any nonzero frequency, , there exists a stable such that
Proof: 2→3
By definition
Use this matrix

## Slide 23: Multiplicative uncertainty robustness margin
Stable weighting systems WL(s) and WR(s) as part of model
  Smallest (linear, dynamic, stable) such that feedback of and C is unstable?
WL
Δ
P
WR
C

## Slide 24: Uncertainty at plant input: alternative models
Independent uncertainty in each input-channel
  diagonal, Δ=diag(Δ1, Δ2,…, Δn)
    independent uncertainty in each actuator (or their effect)
  diagonal, real-valued
    Independent gain variation in each actuator
  diagonal , transfer function, Δ(s) =diag(Δ1(s), Δ2(s),…, Δn(s))
    Independent, unmodeled-dynamics effects in each actuator
For all of these, the Nyquist derivation remains the same. Only the linear algebra needs to be sorted out, specifically:
This minimum-norm root of a determinant problem will occur repeatedly, suggesting a definition to describe this important problem. This is the structured singular value, and will be introduced later.
Same analysis for robustness of stability